## Slide 1
The Story Behind the
22 April 2014
World’s Largest 3D Printed Aircraft
Notes: Jean

## Slide 2: Meet the Team
Tanveer Chandok
Georgia Tech
Michael Kelley
Purdue
Ignacio Jose Benitez Cruz
Purdue
Nicolaus Caniza
Purdue
Roman Esteban Hofer
Purdue
Michael Miles
BYU
Stephen Lutgring
Purdue
Scott Ashcraft
Georgia Tech
Aaron Inouye
BYU
Jean Ruggiero
Purdue
2
Notes: Jean

## Slide 3: Agenda
System overview
Detailed Design
Detailed Analysis
Testing
Manufacturing
Cost Update
Lessons Learned
Conclusion
3
Notes: Jean

## Slide 4: Boeing AerosPACE Course
Multi-university collaboration to produce UAS for agricultural imaging.
4
Notes: Jean

## Slide 5: System Overview
5
Tetracam for agricultural imaging
3D printed skin & internal structure
Winglets for yaw stability
Elevon control surfaces
Avionics bay
Battery compartment
AXI 4130/16 electric motor
Catapult launcher
Notes: Jean

## Slide 6: Specifications
Planform Area: 7.83 ft2
Aspect Ratio: 7.1
Gross Weight: 11.7 lb
Powerplant: AXI 4130/16 w/16x8” prop
6
Notes: Jean

## Slide 7: Mission Overview
Goal: Provide aerial imaging capability for agricultural applications.
Cruise
(1 mile)
Launch & Recovery
(100’ x 100’)
Reserve
(15 min)
Mission Area
(60 acres)
Cruise
(1 mile)
Notes: Jean

## Slide 8: Normalized Difference Vegetation Index
Sample NDVI image of large area taken from GA aircraft.
Notes: Jean

## Slide 9: Detailed Design
9

## Slide 10: Aerodynamics
10
Notes: Mike K
Graphs of WT, CFD, XFLR5

## Slide 11: Structural Layout
11
Main Wing Spar (CF)
Secondary Wing Spar (3D Printed)
Payload Module
Aft Connector
Fwd Body Spar (CF)
Wing Joint Bulkhead
Motor Mount Bulkhead
Elbow Joint
Notes: Mike K

## Slide 12: Propulsion System
12
 | Initial Configuration | Final Configuration
Motor | Hacker A40-12S | AXI 4130/16
Battery | LiPo 3S-3P (20C) | LiPo 6S-1P (50C)
Propeller | 14x10” | 16x8”
Static Thrust | 5 lbs | 8.6 lbs
Final aircraft weight 4 lbs heavier than initial predictions
  New propulsion system was needed for take-off
Notes: Mike K
Motocalc graphs – include old & new systems

## Slide 13: Stability & Control
13

## Slide 14: Weight & Balance
14
CG is located 23.4 in aft of nose for static margin of 15%.
AC
CG
23.4”
26”
Notes: Mike K

## Slide 15: Avionics
15
Motor
ESC
BEC
Battery
GPS
Radio Receiver
Ardupilot
Telemetry
Servos
Tetracam
Avionics wiring diagram shows integration of subsystems.
Notes: Mike K

## Slide 16: Payload
Tetracam ADC Lite & post-processor produce NDVI images.
16
Tetracam ADC Lite
Team 3D NDVI Image
Stitching Software
NDVI Post-Processor
Dead Grass
Healthy Grass
Mulch
Notes: Mike K
Add labels

## Slide 17: Detailed Analysis & Testing
17

## Slide 18: CFD Analysis
18
Streamlines shown in blue
Spanwise flow demonstrated in WT not captured by CFD analysis
Discrepancies between WT, CFD, XFLR5
Notes: Mike M
Flow visualization

## Slide 19: Wind Tunnel Test
19
Test data shows analysis under-predicts drag, over-predicts lift.
Notes: Mike M

## Slide 20: Aerodynamics Analysis & Test
20

## Slide 21: FEA Structural Analysis
Max deflection is 2.5 in.
Single ply wing with 15 lbf tip load.
21
Notes: Mike M

## Slide 22: Structural Test
22
15 lb load shows skin dimpling but no plastic deformation.
Notes: Mike M

## Slide 23: Structural Analysis & Test
23
Initial ANSYS analysis showed 100% error; update shows 20-30%.
Notes: Mike M
Use MATLAB script

## Slide 24: Propulsion Test
24
Chart: Thrust Coefficient
| 0.47817841520741489 | 0.55643680159348985 | 0.59673545767834324 | 0.40560630183279406
Test 2 | 0.038388 | 0.027623 | 0.023769 | 0.039073
Test 3 | 0.059597 | 0.061251 | 0.061701 | 0.063263 | 0.025485 | 0.036365 | 0.04774 | 0.050863 | 0.023127 | 0.031922 | 0.044901 | 0.049089 | 0.019223 | 0.030044 | 0.042983 | 0.047457 | 0.016733 | 0.027316 | 0.039212 | 0.044338
Prof. Sullivan wksht | -0.045857 | -0.036857 | -0.027857 | -0.018857 | -0.0098571 | -0.00085714 | 0.0081429 | 0.017143 | 0.026143 | 0.035143 | 0.044143 | 0.047743 | 0.049543 | 0.053143 | 0.056743 | 0.060343 | 0.062143 | 0.063943 | 0.065743 | 0.067543 | 0.071143 | 0.080143
Motocalc | 0.079998 | 0.078653 | 0.077285 | 0.075741 | 0.074 | 0.07242 | 0.070672 | 0.068759 | 0.066987 | 0.065077 | 0.063138 | 0.061215 | 0.059289 | 0.057212 | 0.055119 | 0.053031 | 0.050805 | 0.048573 | 0.046356 | 0.043999 | 0.041678 | 0.039366 | 0.03708 | 0.034684 | 0.032456 | 0.030124 | 0.027817 | 0.025556 | 0.023332 | 0.021011 | 0.018867 | 0.016764 | 0.014577 | 0.012559 | 0.010462 | 0.0084112 | 0.0065284 | 0.0045705
Test performed with Hacker A40-12S at various airspeeds in WT.
Notes: Mike M

## Slide 25: Flight Test
25
Flight data of foam prototype flying waypoints at GT AMA field.
Notes: Nacho
Telemetry data

## Slide 26: Launcher Test
26
Successful launch of test prototype with catapult launcher.
Notes: Nacho

## Slide 27: Manufacturing
27

## Slide 28: 3D Printing Not Just for Prototyping Anymore!
28
Main sections printed at Stratasys using Fortus 900.
Notes: Nacho

## Slide 29: Fused Deposition Modeling
FDM uses an extruded thermoplastic filament to print parts.
Step 1: STL file
Step 4: Finished part
Step 3: Printer
Step 2: Tool path
29
Notes: Nacho

## Slide 30: Printing Without Support Material
Eliminating support material saves time & money.
45
Notes: Nacho

## Slide 31: Why 3D Printing?
New frontier in aerospace manufacturing
Faster & cheaper than traditional methods
  Reduced man hours
  Little skill needed for assembly
31
Notes: Nacho

## Slide 32: CAD Modeling for FDM
All thin parts (skin, ribs) are modelled as surfaces with 0.012” clearance to account for filament thickness.
Notes: Nick

## Slide 33: Solids vs. Surfaces
Surfaces printed as single layer, solids as honeycomb.
Internal ribs printed with skin
Solid to eliminate support mat’l
Bulkheads at joints
Reinforced skin around payload
Carbon fiber spar
Notes: Nick

## Slide 34: Manufacturing Collaboration
34
BYU: CAD Modeling
GT: Catapult build & test
PU: Final assembly
Notes: Nick

## Slide 35: Tooling & Jigs
Very few jigs required...
35
Notes: Nick

## Slide 36: Assembly
Final assembly required some sanding & drilling but was relatively simple.
36
Notes: Nick

## Slide 37: Bill of Materials (1 of 2)
37
Section | Component | Qty | Details
Structures | L Body | 1 | 3D Printed Part
 | R Body | 1 | 3D Printed Part
 | L Wing | 1 | 3D Printed Part
 | R Wing | 1 | 3D Printed Part
 | L Winglet | 1 | 3D Printed Part
 | R Winglet | 1 | 3D Printed Part
 | L Elevon | 1 | 3D Printed Part
 | R Elevon | 1 | 3D Printed Part
 | Motor Cover | 1 | 3D Printed Part
 | Wing CF Spar | 2 | 0.5” x 32.5"pultruded CF tube spar
 | Body CF Spar | 2 | 0.5" x6" wrapped CF tube spar
Integration | Elevon hinge | 10 | Point hinge
 | Joining plate | 1 | Aluminum rectangular block
 | Joining screws | 2 | Machine screws & washers
 | Elevon set screws | 10 | Small wood screws
 | Torsion pins | 6 | 1/8" x 1" aluminum rod
Payload | NDVI imager | 1 | Tetracam ADC Lite
 | Camera battery | 1 | Zippy 2200 mAh 3S1 25C
 | Video transmitter | 1 | ReadyMadeRC 400mW 1300MHz
 | Payload Module | 1 | Plywood & acrylic shelf unit
Notes: Nick

## Slide 38: Bill of Materials (2 of 2)
Section | Component | Qty | Details
Propulsion | Motor | 1 | AXI 4130/16 electric motor
 | Motor Mount | 1 | Cross mount
 | Mounting Screws | 4 | Screws & washers supplied with motor
 | Mounting Nuts | 4 | Locking nuts
 | Propeller | 1 | 16x8" composite propeller
 | Battery | 1 | Zippy 5000mAh 6S 45C
 | Speed Controller | 1 | Castle phoenix edge lite HV 60
 | Battery Eliminator | 1 | Castle CC BEC 6S
Avionics | Autopilot | 1 | APM 2.5 Ardupilot
 | F-F Cables | 10 | 12 cm avionics wiring cables
 | M-F Cables | 10 | 30 cm servo cables
 | Receiver | 1 | Spektrum AR8000 8-channel
 | Elevon Servo | 2 | Hitec HS-465 MG
 | GPS & Compass | 1 | 3DR uBlox GPS w/ compass kit
 | Radio set | 1 | 3DR radio 915 MHz
38

## Slide 39: Repairability
39
Individual components cannot be repaired, but replacement is fast & easy. In the future, users can print their own at home.
Notes: Nick
New parts will be self-locating and can be replaced by the end user with only a screwdriver.
Printer shown is made for the home user at only $1300

## Slide 40: Cost Update
40
Component | Cost
Payload | $4,500.00
Propulsion | $350.00
Avionics | $750.00
Battery | $130.00
Structure | $300.00
Servos | $170.00
Launch | $800.00
Total | $7,000.00
Notes: Jean

## Slide 41: Lessons Learned
Face-to-face kickoff meeting would be helpful
Define individual responsibilities early
Accountability improves productivity
Agendas improve meeting effectiveness
Schedule lectures & labs so all students can attend
Some private team meetings might lead to better cohesion
41
Notes: Jean

## Slide 42: Collaboration Tools
Used Google Hangouts but prefer Webex
Google Drive was most effective for file sharing
File organization & searching could improve CorpU
42

## Slide 43: Conclusion
Designed & built UAS to satisfy agricultural mission
  Ansys, Star CCM+, Catia, component testing
Gained exposure to FDM
Experienced long-distance collaboration
Notes: Jean

## Slide 44: Acknowledgements
Dr. John Sullivan
Eli Cohen
James Berlin (Stratasys)
The Boeing Company
  Howard Horne
  Adam Hadnott
Notes: Jean

## Slide 45: Questions?
Notes: Jean